## Slide 1: Adaptive Exploration for Geological Classification
Team:
Aishanou Osha Rait
Shivam Gautam
Tushar Agrawal
Bishwamoy Sinha Roy

## Slide 2: Overview
Problem Introduction
Simulation Environment
Aspect 1 – Where to sample
Aspect 2 – How to get to sampling point
Results
Conclusion

## Slide 3: Problem Introduction
Rover exploration of extra-terrestrial bodies is slow
One of the motives of exploration – Rock classification
Spectrometer readings to classify rocks

## Slide 4: Problem Introduction
Satellite Spectrometers have low wavelength and spatial resolution and high sensor noise
Ground based spectrometer sampling is costly
Optimization Problem
Where to sample such that the rock classification has lowest uncertainty.

## Slide 5: Problem Introduction
Select Sampling Point
Sample the point
Plan path to sample point
Update spectrometer data
Two main challenges:
Where to sample
How to get there

## Slide 6: Simulation Environment
Provides three pieces of information
Information 1 – Satellite Reading for a region
  Containing less number of channel
Information 2 – Rover reading at each point in the region
  Result of sampling a point – more number of channels (higher resolution)
Information 3 – True classification of each point
We control
  Noise in sensor
  Number of classes
  Number of dominant and rare classes

## Slide 7: Simulation Environment

## Slide 8: Aspect 1: Where to sample
Method 1: Variance based Entropy

## Slide 9: Aspect 1: Where to sample
Method 1: Feature Space based Entropy

## Slide 10: General Flow
Satellite Data in feature space
Cluster
Probabilities and entropy calculation
Maximum entropy point sample
Replace sampled point with data

## Slide 11: General Flow cont.
Define vector of movement of sampled point
Gaussian around moved point to move near-by points
Update feature space

## Slide 12: Data in Feature Space

## Slide 13: Clustering
K-means
  Parametric approach – assumes number of classes (not available)
Mean-shift
  Non-parametric approach – bandwidth keeps changing
    Optimization parameter – people have done this...
  might not capture the rare classes as they are sparse
Meanshift (0.2)
Kmeans

## Slide 14: Probability and Entropy
i = feature point j = cluster J = total number of clusters
Shannon’s Entropy for each feature point Units – bits (log base 2)

## Slide 15: Re-sampling
Gaussian around sampled point
sigma proportional to distance to closes cluster center

## Slide 16: Results
Overall average entropy decrease in both methods..
2.96% decrease
1.25% decrease

## Slide 17: Aspect 2: How to get to point
Method 1: Multi-Heuristic A*

## Slide 18: Aspect 2: How to get to point
Method 1: DP path length constraint planning